## Slide 1
CrochetCV
AI-Powered Crochet Pattern
Verification & Generation
Bridging Generative AI and Computer Vision
to validate craft patterns humans can trust
Ekaterina Levchenko

## Slide 2
The Problem
AI-generated crochet patterns
are flooding the market
Online marketplaces are full of crochet instructions generated by AI that have never been tested by a real crafter. Buyers pay for patterns that contain impossible stitch combinations, broken repeat sequences, and nonsensical construction steps.
Nobody is checking if these AI patterns actually work.
My Solution: CrochetCV
Generate crochet patterns with Generative AI, then verify them with Computer Vision. A YOLOv8n OBB model detects every stitch symbol, reconstructs the scheme, and enables structural validation.
Generate with AI. Verify with CV. Trust the result.

## Slide 3
System Architecture
User Prompt
Text description
or image upload
Gemini Gen
AI generates
crochet diagram
YOLOv8n OBB
Detect & classify
9 stitch types
Reconstruct
Clean scheme +
JSON export
Verify
Structural check
via DSL graph
Tech Stack: FastAPI | Streamlit | YOLOv8 (Ultralytics) | Google Gemini | CrochetPARADE DSL | Hunyuan3D

## Slide 4
The Core: YOLOv8n OBB Detection
YOLO OBB detections (left) and reconstructed scheme (right)
Why OBB?
Oriented Bounding Boxes
Crochet stitches are rotated symbols. Standard axis-aligned boxes fail; OBB captures angle and shape.
Nano model (YOLOv8n)
Fast enough for real-time web app. Generation takes 20 sec to 2 min depending on complexity.
9 stitch classes
chain, single, double, treble, double treble, half double, fan, ensemble chain, noise

## Slide 5
Adaptive Tiling Strategy
Tile grid with 50 overlapping tiles (190 px effective size)
1
Estimate
Low-confidence YOLO pass to measure median stitch size
2
Calculate
Dynamic tile size so stitches land at ~100 px target resolution
3
Tile & Detect
Overlapping tiles with per-tile inference
4
Merge & NMS
Translate coords back, class-aware deduplication
This enables handling high-density patterns of any size without manual configuration

## Slide 6
Challenges & How I Solved Them
No Dataset
No public oriented bounding box dataset for crochet stitch symbols existed. I manually labeled data, trained an initial model, used it to pre-label more images, then hand-corrected those labels to speed up annotation.
Model Selection
I tried classical CV (HOG + SVM), various architectures, and different detection approaches before converging on YOLOv8n OBB as the best balance of accuracy, speed, and rotated-symbol handling.
Pattern Verification
Proofreading schemes requires building a directional graph of stitch connections. The CrochetPARADE DSL can represent this, but code generation from detected JSON is a complex, ongoing task.

## Slide 7
Data & Training Strategy
1
Manual Labeling
Hand-annotated crochet scheme images with oriented bounding boxes for 9 stitch classes using Label Studio
2
Initial Training
Trained YOLOv8n OBB on the manually labeled dataset to bootstrap the detection pipeline
3
Semi-Auto Labeling
Used the trained model to pre-label new images, then manually corrected the predictions to increase labeling speed
4
Data Synthesis
Attempted synthetic data generation to augment training. While not close enough to replace real data, it contributed to improving the model score

## Slide 8
The Web Application
FastAPI + SSE Backend
Real-time progress streaming
Server-Sent Events for live UI updates
Upload image or type a text prompt
20 sec to 2 min generation time
HTML pattern book output
Dual-path routing: 2D charts vs 3D objects
Streamlit admin page for debugging
Gemini-generated diagram

## Slide 9
Bonus: 3D Amigurumi Path
Gemini reference image
Another example: turtle amigurumi
3D Pipeline
1. Text prompt generates reference image via Gemini
2. Hunyuan3D converts image to 3D mesh (.glb)
3. Mesh is sliced into horizontal rounds
4. Perimeter-to-stitch calibration generates row-by-row amigurumi instructions

## Slide 10
Beyond Crochet
The same pattern applies to any domain where AI generates visual plans and CV verifies them
Architecture
AI generates floor plan layouts. CV reads walls, rooms, and dimensions. Output: validated CAD drawings.
Fashion
AI generates garment sketches. CV extracts pattern pieces and measurements. Output: sewing instructions or 3D model code.
Any Craft Domain
Same framework: generative AI creates, computer vision validates structure, domain-specific DSL enables proofreading.

## Slide 11
Future Work & Takeaways
Next Steps
Pattern verification via CrochetPARADE DSL
  Build directional graph from detected stitches to prove pattern correctness
Auto-fix broken patterns
  Detect structural errors and suggest repairs using the DSL
Expand training data
  Improve synthetic data quality to close the domain gap
Key Takeaways
YOLOv8n OBB is the right tool
for rotated symbol detection in dense craft patterns
Manual labeling was essential
synthetic data helped but couldn't replace real annotations
GenAI + CV is a powerful combo
generate fast, verify reliably, applicable beyond crochet

## Slide 12
Live Demo
crochet.webapp + Streamlit Admin
Generate a pattern | Watch YOLO detect stitches | Explore the reconstructed scheme

## Slide 13
Thank You
Questions?
Ekaterina Levchenko